KDE Wacom Tablet
System Test Specification

Document Version:	1.0
Document State:	Draft
Last Modified:	So, 28. Oktober 2012

# Overview
## Test Environment and Result
Tester:	<put your name and e-mail here>
KDE Wacom Tablet Version:	<which version was tested – e.g. 2.0 RC1>
Xsetwacom Version:	<use 'xsetwacom -V' to determine the version>
Tablet Devices:	<enter name and model of the tablet devices used for this test>
Linux Distribution:	<which distribution (name and version) was used for the test>
Result:	<mark with the appropriate color described below>

Send your test protocol to Alexander Maret-Huskinson <alex@maret.de>
## Instructions
Thank you for helping us to improve the KDE wacom tablet configuration utility! By executing the tests described in this document, you help us to ensure that all features are tested at least on a sanity level. If you find a bug while executing these tests you should add it to the bug tracker (http://bugs.kde.org) and not to this document. Only the bug number is to be added to the column Issues and the test should be marked as failed (with the appropriate color) in the Result column. When done, please send this document to any of the KDE Wacom Tablet developers.

Use the following colors to mark the result of each test in the Result column:
The test failed.
The test passed but there are some issues.
The test passed.
The test could not be executed because the description is insufficient.
The test was not executed (e.g. due to lack of hardware or time).

# Tests
## KDE Daemon Service
Test	Action	Expect	Issues	Result
Start / Stop Daemon	Open KDE's system settings. / Select "Startup and Shutdown" / Select "Service Manager" / Select the Wacom tablet service from the list of services. / Press the "Stop" button (Expect 1) / Press the "Start" button (Expect 2)	The service is stopped without crashing. / The service is started without crashing.

## KCM Module
Test	Action	Expect	Issues	Result
Start Module	Disconnect any tablet devices. / Stop the KDE Tablet Daemon Service. / Open KDE's system settings. / Select the Wacom Tablet Configuration Module (Expect 1). / Close the Wacom Tablet Configuration Module. / Start the KDE Tablet Daemon Service. / Open the Wacom Tablet Configuration Module (Expect 2). / Connect a tablet device (Expect 3). / Disconnect the tablet again (Expect 4).	The module is opened and displays an error message about the daemon not being available. / The module is opened and displays an error message about no tablet being available. / The error message disappears and the configuration options are displayed. / The error message about no tablet being available is displayed again.
Create Profile	Press the "Create New Profile" button (Expect 1). / Press Cancel (Expect 2). / Press the "Create New Profile" button again (Expect 1). / Enter a new profile name and confirm the dialog (Expect 3). / Press the "Create New Profile" button again (Expect 1) / Enter a profile name which already exists and confirm the dialog (Expect 4). / Change some settings of the current profile but do not apply them yet. / Press the "Create New Profile" button again (Expect 1) / Enter a new profile name which does not exist yet and confirm the dialog. (Expect 5). / Save the changes and switch back from the new profile to the previous one. (Expect 6)	A dialog is displayed prompting for a profile name. / The dialog is closed and no profile is created. / A new profile is created and is automatically selected. / The dialog is closed but no profile is created. / A prompt is displayed, allowing the user to apply unsaved changes. / The unsaved changes were successfully saved.
Switch Profile	Change some settings of the current profile but do not save them yet. / Switch to a different profile (Expect 1). / Save the changes. (Expect 2) / Switch back to the previous profile (Expect 3). / Change settings from different tabs, apply them and switch profiles back and forth (Expect 3).	A prompt is displayed allowing the user to save unsaved changes. / The changes are saved and the profile is switched to the selected one. / The profile settings were successfully saved.
Delete Profile	Press the delete profile button (Expect 1)	The current profile is deleted and a different profile is selected.
General Tab
Shortcuts	Make sure a tablet is connected. / Assign a keyboard shortcut to each shortcut action and apply the changes. / Press each keyboard shortcut (Expect 1).	The shortcut triggers the corresponding action.
Pen Tab
Eraser Feel	Use xsetwacom to query the current value of the eraser device's "Threshold" parameter. / Use the slider to change the eraser feel and apply the changes. / Use xsetwacom to query the "Threshold" parameter of the eraser device again (Expect 1).	The value changed.
Eraser Pressure Curve	Use xsetwacom to query the current value of the eraser's "PressureCurve" parameter. / Press the "Edit Pressure Curve" button (Expect 1). / Change the pressure curve, confirm the dialog with ok and apply the changes. / Use xsetwacom to query the "PressureCurve" parameter of the eraser device again (Expect 2).	A dialog appears which allows the user to edit the pressure curve. / The value changed.
Button Settings	Make sure "use Hover Click" from the "Cursor Settings" is disabled. / Assign any action to Button 2 & 3 and apply the changes. / Move the pen in range of the tablet and press each button (Expect 1). / Repeat the procedure for each possible action.	The button triggers the assigned action.
Cursor Settings – Hover Click	Enable "use Hover Click" and apply the changes. / Move the stylus in range of the tablet but make sure you do not touch the surface. / Press one of the stylus' buttons (Expect 1). / Press the button again, hold it down and touch the tablet's surface with the tip of the pen (Expect 2).	The button's action is not triggered. / The button's action is triggered.
Cursor Settings – Mode	Set the mode to absolute and apply the changes. / Move the Stylus to different areas of the tablet and watch the mouse cursor (Expect 1). / Set the mode to relative and apply the changes. / Move the Stylus to different areas of the tablet and watch the mouse cursor (Expect 2)	The tablet area is mapped to the screen area and the cursor behaves accordingly. / The tablet area is not mapped to the whole screen but behaves like a mouse cursor.
Tip Feel	Use xsetwacom to query the current value of the stylus device's "Threshold" parameter. / Use the slider to change the tip feel and apply the changes. / Use xsetwacom to query the "Threshold" parameter of the stylus device again (Expect 1).	The value changed.
Tip Pressure Curve	Use xsetwacom to query the current value of the stylus' "PressureCurve" parameter. / Press the "Edit Pressure Curve" button (Expect 1). / Change the pressure curve, confirm the dialog with ok and apply the changes. / Use xsetwacom to query the "PressureCurve" parameter of the stylus device again (Expect 2).	A dialog appears which allows the user to edit the pressure curve. / The value changed.
Pad Buttons Tab
Express Keys	Assign "Button 1" to each express key and save the changes. / Open "dolphin" and use your mouse and the express keys to navigate (Expect 1) / Assign a simple key to each express key and apply the changes. / Open "kate", place the cursor in the text field and press each express key (Expect 2) / Disable each express key and apply the changes. / Go back to kate and press each express key (Expect 3) / Play with the settings and assign different shortcut key combinations to the express keys. Apply the changes and use any application to test your settings (Expect 4).	The express keys can be used as left mouse button. / Pressing the express key adds the assigned key to kate. / Pressing the express key triggers no action. / Pressing the express key triggers the assigned shortcut.
Touch Strip	Connect a tablet with a touch strip. / Repeat the actions from the Express Keys Test (Expect 1)	The strip actions work as expected.
Touch Ring	Connect a tablet with a touch ring. / Repeat the actions from the Express Keys Test (Expect 1)	The touch ring works as expected.
Wheel	Connect a tablet with a wheel. / Repeat the actions from the Express Keys Test (Expect 2)	The wheel works as expected.
Touch Tab
Touch Events	Connect a tablet with touch capability. / Disable touch events in the General group and apply the changes (Expect 1) / Enable touch events and apply the changes (Expect 2)	It is no longer possible to use the pad as a touchpad. / The pad can be used as a touchpad again.
Invert Scroll	Connect a tablet with touch capability. / Disable the "Invert scroll direction" checkbox and apply the changes. / Move the cursor into this document so the window is active. / Scroll the document by placing two fingers on your tablet moving them up and down (Expect 1). / Enable "Invert scroll direction" and apply the changes. / Scroll the document again (Expect 2)	The document is scrolled the same way you would move a sheet of paper. / The scroll direction is inverted.
Mode	Connect a tablet with touch capability. / Select the "Absolute" radio button from the "General" group and apply the changes. / Touch different areas of your tablet (Expect 1) / Select the "Relative" radio button from the "General" group and apply the changes. / Touch different areas of your tablet and move your finger on the tablet. (Expect 2)	The tablet area is mapped to the screen and the cursor jumps to the corresponding position of the screen when touching the tablet. / The tablet area is no longer mapped to the screen area and the cursor behaves like a normal mouse cursor.
Gestures	Connect a tablet with touch capability. / Make sure Touch events are enabled in the "General" group. / Uncheck the "Enable Gestures" checkbox and apply the changes. / Click into this document and then use two fingers on your tablet and move them up and down in parallel. (Exepect 1) / Check the "Enable Gestures" checkbox and apply the changes. / Click into this document again and try to scroll with the scroll gesture again. (Exepect 2)	The document does not scroll, only the mouse cursor moves. / The document is scrolled up and down according to the movement of your fingers.
Zoom Distance / Scroll Distance / Tap Time	Connect a tablet with touch capability. / Use xsetwacom to query the parameter "ZoomDistance" of your touch device. / Change the "Zoom Distance" value in the Multi-Touch group and apply the changes. / Use xsetwacom to query the parameter again. (Expect 1) / Repeat steps 1-4 with the xsetwacom parameters "ScrollDistance" and "TapTime".	The value changed to the one entered into the input field.
Pad Mapping
Orientation	Select "none" from the Rotation drop-down menu and apply the changes. (Expect 1) / Select "clockwise" from the Rotation drop-down menu and apply the changes (Expect 2). / Select "counter clockwise" from the Rotation drop-down menu and apply the changes (Expect 3). / Select "half" from the Rotation drop-down menu and apply the changes (Expect 4).	Stylus and Eraser controls behave normally. / Stylus and Eraser controls are rotated clockwise. / Stylus and Eraser controls are rotated counter clockwise. / Stylus and Eraser controls are upside down.
Auto-Rotate	Connect a screen which supports rotation. / Enable the "Rotate with screen" checkbox and apply the changes. / Rotate your screen. (Expect 1)	The tablet controls are rotated according to the screen orientation.
Screen Area / (Single Monitor)	Make sure your pen operates in absolute mode. / Select "Part of the Screen" from the "Screen Area" group and use the red box on the right to define the part of the screen which is to be mapped. Apply the changes. (Expect 1) / Switch pen mode to relative mode (Expect 2) / Switch pen mode back to absolute mode (Expect 1). / Change screen area mapping back to "Full screen" (Expect 3).	The tablet area is mapped to the corresponding part of the screen. / The tablet can be used to move the mouse cursor freely again. / The tablet is mapped to the whole screen again.
Screen Area / (Multi Monitor)	Connect a second monitor and make sure you pen operates in absolute mode. / Map the screen area to one of the screens and apply the changes. (Expect 1) / Map the screen are to the other screen and apply the changes. (Expect 1) / Map the tablet to "Part of the screen" and select a range which covers both monitors. Apply the changes. (Expect 2)	The tablet is mapped to the configured screen. / The tablet is mapped to the configured screen area.
Tablet Area / (Single Monitor)	Make sure your pen operates in absolute mode and the Screen Area is set to "Full screen" / Select "Part of the tablet" from the "Tablet Area" group and use the red box on the right to select an area of your tablet. Apply the changes. (Expect 1) / Select "Part of the screen" from the "Screen Area" group and configure a screen area. Apply the changes. (Expect 2) / Select the "Force Proportions" checkbox (Expect 3). / Select "Full Tablet" from the "Tablet Area" group and apply the changes.	The screen is mapped to the configured tablet area. / The configured tablet area is mapped to the configured screen area. / The red tablet area selection box is adjusted to match the proportions of the red screen area box. / The full tablet area is mapped to the configured screen area.
Tablet Area / (Multi Monitor)	Repeat the tests from the single monitor section but make sure all selected screen areas cover multiple monitors. (Expect 1)	Expect results from single monitor test.
Calibrate	Make sure your pen operates in absolute mode. / Press the calibrate button. (Expect 1) / Press Escape (Expect 2) / Press the calibrate button (Expect 1) / Follow the instructions on the screen. (Expect 3) / Apply the changes (Expect 4)	A fullscreen calibration window opens. / The window closes / The window closes and the red area box marks the calibrated area. / Your tablet is properly calibrated.
Touch Mapping
Touch Mapping	Repeat the tests from the Pad Mapping section only with touch in mind.	The features work as expected.

## Applet
Test	Action	Expect	Issues	Result
Add Applet with no services or tablets being available.	Disconnect any tablet devices. / Stop the KDE Tablet Daemon Service. / Right click on the desktop. / Select "Unlock Widgets" if your widgets are currently locked. / Right click again and select "Add Widgets" / Select the Wacom Tablet Applet from the widget selection dialog (Expect 1). / Start the KDE Tablet Daemon Service (Expect 2). / Connect a tablet device (Expect 3).	The applet is added to the desktop. The applet shows an error message about the tablet daemon not being available. / The applet shows an error about no tablet being connected. / The applet configuration settings become available.
Remove Applet	Make sure a tablet is connected and the applet was added to the desktop. / Remove the applet from the desktop (Expect 1 & 2). / Remove the tablet. (Expect 2) / Add the applet to the desktop again (Expect 3) / Remove the applet form the desktop (Expect 1 & 2).	The applet is removed from the desktop without crashing. / The plasma-desktop does not crash. / An error message about no tablet being connected is displayed.
Add Applet with all services being available.	Make sure the KDE Tablet Daemon Service is running and a tablet is connected. / Use the Wacom Tablet Configuration Module to activate a profile other than the default profile. / Add the Wacom Tablet Applet to the desktop (Expect 1 & 2). / Use the Wacom Tablet Configuration Module to switch to different profiles and change the settings of an active profile. Press Apply to apply these changes and watch how the applet configuration widgets change (Expect 2).	The tablet applet is added to the desktop and no error messages are displayed. / The correct profile is selected and the configuration options currently selected match those of the profile.
Select Profile	Connect a tablet device. / Select a profile from the drop down (Expect 1). / Select a different profile (Expect 1).	The profile is activated and the applet's configuration widgets are set according to the profile's settings.
Enable / Disable Touch	Connect a touch-cabable tablet device. / Toggle the Touch radio button to off (Expect 1) / Toggle the Touch radion button to on (Expect 2)	The touch feature of the tablet is turned off. / The touch feature of the tablet is turned on.
Manual Rotation	Connect a tablet device preferably with touch capability. / Press the rotate-left button (Expect 1) / Press the rotate-right button (Expect 2) / Press the rotate-half button (Expect 3) / Press the reset-rotate button (Expect 4) / Select each option and then press the same button again (Expect 5).	Stylus, Eraser and Touch controls are rotated counter clock wise. / Stylus, Eraser and Touch controls are rotated clock wise. / Stylus, Eraser and Touch controls are rotated upside down. / Stylus, Eraser and Touch controls are back to normal. / Nothing changes.
Mode Switch	Connect a tablet device preferably with touch capability. / Toggle Mode to "Absolute" (Expect 1) / Toggle Mode to "Relative" (Expect 2) / Toggle back to "Absolute" (Expect 1)	Stylus and Eraser mode is switched to absolute; Touch mode is unchanged. / Stylus and Eraser mode is switched to relative; Touch mode is unchanged.
Settings Dialog	Connect a tablet device. / Open the settings dialog by pressing the settings icon of the plasma widget (Expect 1). / Cancel the settings dialog (Expect 2). / Open the settings dialog again (Expect 1). / Change different type of settings like the profile, the touch mode, etc. and confirm the changes with the ok button. (Expect 3). / Disconnect the tablet. / Open the settings dialog again (Expect 4).	The KCM settings dialog is displayed with the currently selected profile. / The dialog is closed without crashing and no changes are applied to the current tablet settings. / The changes are applied and the applet's configuration widgets are updated accordingly. / The settings dialog is opened but displays an error message about no tablet being available.